Product Description
Geiger Muller counter/GM tube M4011
Geiger Muller tube J302,for deatail please contact us
Model M4011 countertube
The detector is oxide cathode tube,coaxial cylindrical structure of thin walled(the denity of tube wall50±10cg/cm2),the Pulse application-oriented halogen tube,The ambient temperature from -40°C~55°C range that is exploring 20mR/h-120mR/hγ-ray and 100~1800 off variables/min.cm 2 softβ-ray.
Diameter: Φ10±0.5mm
Length: 90±2mm
Starting voltage:<350V
Minimum plateau rang:80v
Maximum plateau slope:10%/80v
Recommended working voltage: 380V
Maximum count rate:25times/min
Limit working voltage: 550V
Life expectancy: >1×109pulse
Keep shell clean
The countetube should keep a high clean,.To minimize surface contamination,otherwise it will reduce the insulation resistance.
Apply the typical working conditions
The characteristic parameters of counter are measured under the recommended operating voltage.so the user should be possible to use the recommended operationg voltage to obtain the given parameters.
Installation with caution
When you installation the counter should pay attention to it,as counter output leads as short as possible.Andode and cathode leads to extremely excessive force shall not be.Especially the tube of glass shell should be careful,otherwise it will cause the pipe leak or shell broken.